## Slide 1
Presented By:
George Noel – Volpe
Mark Glaze - FHWA
1/13/2014
MOVES Project Level Sensitivity Analysis Update
Transportation Research Board 93rd Annual Meeting
Transportation and Air Quality Committee, ADC20

## Slide 2: History of MOVES Sensitivity Analysis
MOVES Project Level Analysis Began in November 2012
  Is a complement analysis to the Regional Level Sensitivity Analysis – Report released in December 2012
Focused on three variables associated with the Project Level Domain
  Age Distribution
  Fleet Mixture (Link Source Type)
  MOVES Drive Schedules
    Average Speed, Link Drive Schedule, and Operating Mode Distribution
Coordinate with NCHRP 25-38 to avoid overlapping analyses
Volpe to complete draft report January 2014 and final report release March 2014

## Slide 3: Age Distribution Analysis
The Project Level applied more meaningful variations
  Reached out to the Transportation Planning Board (TPB) of the Metropolitan Washington Council of Governments (MWCOG)
  Provided Age Distribution data for each MOVES source type
  For each source type analyzed, divided the Age Distribution into age groups based upon the trends observed from the TPB of MWCOG data.
Analyzed the effects of vehicle aging on Passenger Cars, Transit Buses, Single Unit Trucks and Combination Trucks

## Slide 4: Age Distribution Passenger Car Analysis and Results
Source Type | Pollutant | Case | Average Age | Emission Rate (gram/vehicle-mile) | Percent Change
Passenger Car | NOX | Baseline | 7.48 | 0.2929 | -
 |  | Scenario 1 | 7.68 | 0.3017 | 2.91%
 |  | Scenario 2 | 7.86 | 0.3104 | 5.63%
 |  | Scenario 3 | 8.21 | 0.3246 | 9.76%
 |  | Scenario 4 | 8.53 | 0.3367 | 12.99%
 |  | Scenario 5 | 9.24 | 0.37 | 20.84%
Passenger Car |  |  |  |  |  | 
Vehicle Age Range | Baseline Age Fraction | Scenario 1 | Scenario 2 | Scenario 3 | Scenario 4 | Scenario 5
0-3 years | 0.32 | -5% | -10% | -20% | -30% | -45%
4-7 years | 0.22 | -2% | -5% | -7.50% | -10% | -20%
8-12 years | 0.26 | 5% | 10% | 20% | 30% | 50%
13-17 years | 0.14 | 4% | 8% | 15% | 20% | 30%
18-30 years | 0.06 | 2.50% | 5% | 7.50% | 10% | 25%
Average Vehicle Age | 7.48 | 7.68 | 7.86 | 8.21 | 8.53 | 9.24

## Slide 5: Fleet Mix (Link Source Type)
Conduct Fleet Mix Sensitivity Analysis for multiple cases
  Geographic Area Data Source
  Passenger Car to Passenger Truck Ratio
  Heavy Duty Truck Mix
  Heavy Duty Truck Type Mix
  Transit Bus Mix
  Utilized Fleet Mix data provided by Georgia Tech
Compared composite emissions rates to the ‘Baseline Case’ specific to the scenario/cases that were analyzed

## Slide 6: Fleet Mix Geographic Area Data Source Results

## Slide 7: Average Speed compared to Drive Schedule and Operating Mode Distribution
The Project Level Sensitivity Analysis compared using Average Speed for defining a link to:
  Highway Capacity Manual (HCM) derived Drive Schedule/Operating Mode Distributions
  Trip based Empirical Data provided by Georgia Tech
  Link Types analyzed
    Cruise Conditions
      Arterial
      Freeway
    Intersection Links
      Approach
      Queue
      Acceleration

## Slide 8: Example: MOVES Default Drive Schedules

## Slide 9: Average Speed
The user will specify an average speed for a link
  The average speed and distance assigned to the link determines the Source Operating Hours spent of the link.
  The average speed should represent the conditions of the roadway segment being analyzed
  The Average Speed approach utilizes embedded MOVES drive schedules in the Default Database

## Slide 10: Average Speed compared to constant approach speed Drive Schedule
Road Type | Link Type | Scenario | CO Emissions Rates (gram/veh-mile) | Percent Change Compared to Average Speed | PM2.5 Emissions Rates (gram/veh-mile) | Percent Change Compared to Average Speed
Urban Unrestricted Access | Approach | 25 mph Average Speed | 3.6880 | -27.12% | 0.0504 | -36.64%
 |  | Constant 25 mph Drive Schedule | 2.6876 |  | 0.0320 | 
Urban Unrestricted Access | Approach | 35 mph Average Speed | 3.1387 | -24.33% | 0.0374 | -38.41%
 |  | Constant 35 mph Drive Schedule | 2.3752 |  | 0.0230 | 
Urban Unrestricted Access | Approach | 45 mph Average Speed | 2.7569 | -19.77% | 0.0314 | -35.52%
 |  | Constant 45 mph Drive Schedule | 2.2118 |  | 0.0203 | 

## Slide 11: Project Level Sensitivity Results Summary
Variations in Age Distribution can have a significant effect on emissions rates
  An older average age does not always equate to higher emissions rates (Transit Bus Scenario)
  For passenger cars when the average age increases by a year then the emissions rates increase was in the 10% percent range for CO, VOC, and NOX. The emissions rate increase in PM2.5 was approximately 5%.
Getting the fleet mix accurate for your project is important
  The ratio between passenger cars and passenger trucks is important primarily for CO
  Getting the ratios between single unit and combination trucks are important
  However there is very little change in emissions rates between the short haul and long haul designations
  Observed slightly lower emissions rates when increasing proportion of long-haul vehicle types for NOX and PM2.5.
Still analyzing average speed compared to link drive schedule and operating mode distribution

## Slide 12: Sensitivity Questions – Drive Schedule
What is the difference in emissions rates between using average speed versus user provided link drive schedule/operating mode distribution?
  The default drive schedules utilized when using average speed might not represent the exact profile you want to model
    Link might only have deceleration and idle
    Link might only have cruise with no deceleration or acceleration
How detailed do you have to be?
  Individual drive schedules for each vehicle on the link?
  Does it matter if you are more detailed?