## Slide 1
Utilizing Traffic Simulation Tools with MOVES and AERMOD
Extended Abstract 2011-A-717-AWMA
Presented by George Noel, Dr. Roger Wayson, and Adam Klauber

## Slide 2
Overview
Quantify the emissions and fuel consumption associated with traffic congestion from Commercial Motor Vehicle (CMV) crashes
Project Description
Traffic Simulation
Emissions Analysis
Future Use with Dispersion Analysis

## Slide 3: Field CMV Crash Delay Data
All States contacted for crash data – Kentucky and Pennsylvania contributed statewide CMV crash closure duration and location data
Attribute | Kentucky | Pennsylvania
Location | Road mile marker | Latitude/longitude
Duration | Discreet value of lane closure | 7 range values for incident (e.g. 0-30 min.)
Severity | Fatal, Injury, Property Damage Only (PDO) | Fatal, Injury, PDO
Truck type | No data | Yes
Urban/rural distinction | As defined by Kentucky State Highway Patrol | As defined by PennDOT
Vehicle configuration | 4 truck types, 2 bus types | 7 truck types, 2 bus types
Other relevant data | Hazmat presence, other involved vehicles | # injuries/fatalities, Hazmat presence

## Slide 4: CMV Crash Delay TSIS-CORSIM Tool
TSIS (Traffic Software Integrated System) CORSIM (CORridor-microscopic SIMulation program) version 6.2 (Feb. 2010)
  Components
    NETSIM for urban streets (or rural non-freeway)
    FREESIM for freeways
  Investigation Sequence
    Simulation Design → Translation → Processing → Outputs
TSIS-CORSIM TOOL
NETSIM
FRESIM
TRAFED or
Coding
CORSIM
TRAVU (Animation)
Text Editor (Code)

## Slide 5: Problem: Emissions Traffic Modeling Did Not Directly Align with Emissions Modeling
Emissions estimations relied on simplistic vehicle performance (MOBILE)
  Constant velocities
  Non-validated idling times
  Limited set of pre-defined drive cycles
What happened with emissions values?
  Non-alignment with traffic simulations
  Low fuel burn estimates (paradoxical results)
  Low nitrous oxides (NOx) estimates
Vehicle Drive Cycle Example
From: http://www.daham.org/basil/leedswww/emissions/drivecycles.htm

## Slide 6: Solution: Traffic Simulation Animation Files to Provide Vehicle Specific Power
Inquiries to subject matter experts revealed possible solution
Obtain animation file vehicle time-step data from traffic simulation
Translate vehicle performance (in binary code) to database via Volpe Center developed parser tool. Actual performance factors:
  Vehicle aerodynamic drag
  Road surface friction
  Inertia forces
Utilize vehicle specific power equation to calculate more accurate engine performance
Run US EPA MOVES model on project level to obtain associated emissions estimates
From: Jimenez, J et .al. “Vehicle Specific Power: A Useful Parameter
for Remote Sensing and Emission Studies” 1999

## Slide 7: Traffic Simulations Overview
Traffic Simulation runs (TSIS CORSIM tool – version 6.2)
  Baseline cases (without crashes) Monte Carlo 10 runs each
  Crash scenarios, Monte Carlo 40 runs each
    Full closures (15 minutes; 1½ hour; 4 hr) diversions for longer 2 runs
    Partial closures (same durations as full closure)
  Network configurations
    Expressway, urban & rural (without surface network)
    Arterial, urban only (with connected expressway)
    Other, urban & rural local/collector/minor arterial (with connected expressways)

## Slide 8: Traffic Simulation Details
Baseline Scenario Runs
  Facilities 5 representational categories
  Volumes (50-6,000 vehicles per hour)
  Lane Number range (2-6 bi-directional) HPMS data
  Fleet Composition
  Speeds Freeflow (HPMS data)
Crash Scenario Runs
  Baseline Facility, Volume, Freeflow, Volumes, Fleets, and Speeds
  Land closure durations (Kentucky and Pennsylvania Field Data)
  Partial and Full Closures
  Rubber-necking Factor (ORNL research)
Baseline Scenario
Crash Scenario

## Slide 9: Traffic Simulation Details
Scenario Observed Requirements
  Roadway length sufficient to contain traffic queues
  Extended duration road and lane closures
    Freeway utilizes TSIS-CORSIM incident feature
    Non-freeway necessitated alternative introduced measures (e.g. dummy traffic controls, etc.)
  Deterministic vehicle/driver performance for diverted traffic
Traffic Simulations Output
  Delay distributions (median value selected) baseline delay subtracted
  Animation files for translation to time-step data (TSD)

## Slide 10: Emissions Analysis
Emissions Analysis Methodology
  Parsing of TSIS-CORSIM Binary Files
    Utilize Parser Application developed by Volpe
    Parser reads second by second CORSIM animation file data and calculates VSP
    VSP is calculated for each Link and separated by vehicle type
  Motor Vehicle Emission Simulator (MOVES) 2010a
    Parser Application creates an output table that utilizes MOVES Operating Mode Distribution feature
    Operating Mode Distribution determines drive cycle across each link for each vehicle type by hour
  Emissions Analysis
    Incident minus Baseline to estimate the emissions impacts

## Slide 11: Parsing of TSIS-CORSIM Binary Files
TSIS-CORSIM Binary Files
  Utilized for the TRAFVU component for visualizing the simulation
  Contains information for each vehicle at a 1 second resolution
  Contains aggregated information for each time interval assigned by the user
Parsing Application Developed to Translate Binary Output
  Time Step Data Files (TSD) - Individual Vehicle data

## Slide 12: CORSIM to MOVES Mapping
CORSIM | MOVES |  |  |  |  |  | 
Vehcile_Type | sourcetypeID | rollingTermA | rotatingTermB | dragTermC | sourceMass | fixedMassFactor | sourceTypeName
1 | 21 | 0.156461 | 0.00200193 | 0.000492646 | 1.4788 | 1.4788 | Passenger Car
2 | 21 | 0.156461 | 0.00200193 | 0.000492646 | 1.4788 | 1.4788 | Passenger Car
3 | 52 | 0.561933 | 0 | 0.00160302 | 7.64159 | 17.1 | Single Unit Short-haul Truck
4 | 52 | 0.561933 | 0 | 0.00160302 | 7.64159 | 17.1 | Single Unit Short-haul Truck
5 | 52 | 0.561933 | 0 | 0.00160302 | 7.64159 | 17.1 | Single Unit Short-haul Truck
6 | 62 | 2.08126 | 0 | 0.00418844 | 31.4038 | 17.1 | Combination Long-haul Truck
8 | 21 | 0.156461 | 0.00200193 | 0.000492646 | 1.4788 | 1.4788 | Passenger Car
9 | 21 | 0.156461 | 0.00200193 | 0.000492646 | 1.4788 | 1.4788 | Passenger Car

## Slide 13: VSP Parameters
Link | SourceType | OpMode | Desc | Count
810082 | 21 | 0 | Braking | 0.00
810082 | 21 | 1 | Idling | 0.00
810082 | 21 | 11 | Low Speed Coasting; VSP< 0;1<=Speed<25 | 0.00
810082 | 21 | 12 | Cruise/Acceleration; 0<=VSP< 3; 1<=Speed<25 | 0.00
810082 | 21 | 13 | Cruise/Acceleration; 3<=VSP< 6; 1<=Speed<25 | 0.00
810082 | 21 | 14 | Cruise/Acceleration; 6<=VSP< 9; 1<=Speed<25 | 0.00
810082 | 21 | 15 | Cruise/Acceleration; 9<=VSP<12; 1<=Speed<25 | 0.00
810082 | 21 | 16 | Cruise/Acceleration; 12<=VSP;1<=Speed<25 | 0.00
810082 | 21 | 21 | Moderate Speed Coasting; VSP< 0; 25<=Speed<50 | 0.00
810082 | 21 | 22 | Cruise/Acceleration; 0<=VSP< 3; 25<=Speed<50 | 0.00
810082 | 21 | 23 | Cruise/Acceleration; 3<=VSP< 6; 25<=Speed<50 | 0.00
810082 | 21 | 24 | Cruise/Acceleration; 6<=VSP< 9; 25<=Speed<50 | 0.00
810082 | 21 | 25 | Cruise/Acceleration; 9<=VSP<12; 25<=Speed<50 | 0.00
810082 | 21 | 27 | Cruise/Acceleration; 12<=VSP; 25<=Speed<50 | 0.00
810082 | 21 | 28 | Cruise/Acceleration; 18<=VSP<24; 25<=Speed<50 | 0.00
810082 | 21 | 29 | Cruise/Acceleration; 24<=VSP<30; 25<=Speed<50 | 0.00
810082 | 21 | 30 | Cruise/Acceleration; 30<=VSP; 25<=Speed<50 | 0.00
810082 | 21 | 33 | Cruise/Acceleration; VSP< 6; 50<=Speed | 0.04
810082 | 21 | 35 | Cruise/Acceleration; 6<=VSP<12; 50<=Speed | 0.49
810082 | 21 | 37 | Cruise/Acceleration; 12<=VSP<18; 50<=Speed | 0.43
810082 | 21 | 38 | Cruise/Acceleration; 18<=VSP<24; 50<=Speed | 0.03
810082 | 21 | 39 | Cruise/Acceleration; 24<=VSP<30; 50<=Speed | 0.01
810082 | 21 | 40 | Cruise/Acceleration; 30<=VSP; 50<=Speed | 0.00

## Slide 14: Operating Mode Distribution – Free Flow
Chart: Baseline OpMode Distribution
| 0 | 1 | 11 | 12 | 13 | 14 | 15 | 16 | 21 | 22 | 23 | 24 | 25 | 27 | 28 | 29 | 30 | 33 | 35 | 37 | 38 | 39 | 40
OpMode | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2.8121e-05 | 0 | 1.8747e-06 | 5.6241e-06 | 0 | 5.6241e-06 | 1.1248e-05 | 0 | 3.7494e-06 | 0.088758 | 0.57752 | 0.27362 | 0.021469 | 0.01924 | 0.019334

## Slide 15: Operating Mode Distribution – Congestion
Chart: Partial Closure OpMode Distribution
| 0 | 1 | 11 | 12 | 13 | 14 | 15 | 16 | 21 | 22 | 23 | 24 | 25 | 27 | 28 | 29 | 30 | 33 | 35 | 37 | 38 | 39 | 40
OpMode | 0 | 0.19163 | 0.10289 | 0.18575 | 0.020582 | 0.0078708 | 0.0035581 | 0.003826 | 0.0049231 | 1.9626e-06 | 1.9626e-06 | 5.8877e-06 | 7.8502e-06 | 9.8128e-06 | 1.3738e-05 | 2.4532e-05 | 2.6494e-05 | 0.047137 | 0.27215 | 0.13067 | 0.010068 | 0.0096116 | 0.0092397

## Slide 16: Emissions Results
Urban Interstate
Duration = 90 min Partial and Full Closure
Closure | Volume | CO2 (grams) | CO (grams) | NOx (grams) | Energy (MMBtu) | PM10 (grams) | PM25 (grams) | SO2 (grams) | HC (grams) | VOC (grams)
Partial | 1000 | 43296 | 1452 | -19 | 0 | 8 | 7 | 2 | 29 | 27
Full | 1000 | 2555818 | 15339 | 4877 | 30 | 305 | 293 | 46 | 1691 | 1657
Partial | 2000 | 6631950 | 49575 | 17125 | 83 | 911 | 876 | 114 | 3163 | 3090
Full | 2000 | 18126560 | 121890 | 38918 | 225 | 2360 | 2270 | 320 | 11087 | 10846
Partial | 3000 | 21131530 | 150437 | 54987 | 265 | 2862 | 2753 | 361 | 10016 | 9790
Full | 3000 | 38901130 | 266171 | 84789 | 488 | 5175 | 4973 | 689 | 23796 | 23272

## Slide 17: Dispersion Considerations
Nomenclature problem
  Traffic links
  Emission links
  Dispersion links
Emission allocation into AERMOD is not as straight forward as the MOBILE to CAL3QHCR input

## Slide 18: Dispersion Considerations (cont)
Specific Emission Problems
  When area sources are used, there is not a direct connect with MOVES and AERMOD (units of mass/time-area vs. mass/time)
  Determination of traffic link output to emission link input/output and dispersion link input requires considerable pre-planning by analyst (e.g., idle contribution at an intersection; where, how much, vehicle mode)

## Slide 19: Dispersion Considerations (cont)
Dispersion Specific Issues
  Best way to approximate the line source using either volume or area sources
  Methodologies for input of initial plume parameters into AERMOD needs to be improved
  Chemistry (e.g., NO2/NOX ratio, HAPS)
  Consistent input between among users to meet the needs of reviewers
  Inconsistencies at near field receptor locations
  Need for verification

## Slide 20: Acknowledgments
Project Sponsor
  Federal Motor Carriers Safety Administration (FMCSA) – Michael Johnsen
Technical Support
  Federal Highway Administration (FHWA) – Joon Byun
  University of Florida McTrans Center