## Slide 1
MOVES Project Level Sensitivity Analysis
George Noel and Dr. Roger Wayson
The National Transportation Systems Center
Advancing transportation innovation for the public good
U.S. Department of Transportation
Office of the Secretary of Transportation
John A. Volpe National Transportation Systems Center
107th Air & Waste Management Association Annual Conference and Exhibition
Paper # 33650
June 26th, 2014

## Slide 2: Overview
Background
Analysis
  Age Distribution
  Fleet Mixture
  Average Speed compared to user defined Operating Mode Distributions
Results
Findings
Questions

## Slide 3: Background
Project sponsored by Federal Highway Administration (FHWA)
MOVES Regional Level Sensitivity Analysis
  Report released in December of 2012
MOVES Project Level Sensitivity Analysis
  Was a follow up analysis to the Regional Level Sensitivity Analysis
  Parameters chosen to be analyzed for the Project Level analysis were based on some of the finings from the Regional Level Analysis
  Final Report completed in March
Notes: Highlight the Regional level analysis and how it was presented at A&WMA in 2012 in San Antonio.
Also the Regional level was used to determine the input parameters we analyzed for the project level analysis

## Slide 4: Age Distribution
Age Distribution was analyzed for the Regional Level Sensitivity Analysis
The Project Level Analysis applied more meaningful variations
  Reached out to the Metropolitan Washington Council of Governments (MWCOG) to obtain data.
Analyzed multiple vehicle types
  Passenger Cars
  Transit Buses
  Single Unit Trucks
  Combination Trucks
Notes: When Age Distribution was analyzed in the Regional Sensitivity we used arbitrary values to test the senstivity. For the project level we wanted to be more realistic.
We reached out to an MPO to get real world data. We used that real world data to obtain more realistic vairaions

## Slide 5: Age Distribution
MWCOG provided data for 2005, 2008, and 2011
The data showed the fleet aging throughout the years

## Slide 6: Passenger Car Age Distribution Trends
More variable for newer model years
Less variable for latter years
Age Groupings were based on these observed trends
Notes: Point out the blue line being the national default

## Slide 7: Passenger Car Age Distribution Groupings
Vehicle Age Range | Baseline Age Fractions | Scenario 1 | Scenario 2 | Scenario 3 | Scenario 4 | Scenario 5
0-3 years | 0.32 | -5% | -10% | -20% | -30% | -45%
4-7 years | 0.22 | -2% | -5% | -7.50% | -10% | -20%
8-12 years | 0.26 | +5% | +10% | +20% | +30% | +50%
13-17 years | 0.14 | +4% | +8% | +15% | +20% | +30%
18-30 years | 0.06 | +2.5% | +5% | +7.5% | +10% | +25%
Average Vehicle Age | 7.48 | 7.68 | 7.86 | 8.21 | 8.53 | 9.24
Passenger Cars were put into five age groups
Five Scenarios were analyzed
Scenario 1 has the least amount of variation based upon the observed data
Scenario 5 has the highest amount of variation base upon the observed data
Notes: Also mention that we are aging the fleet in each scenario.
Also highlight that these ranges are realistic. Even in scenario 5 we did observed some model years have that much variation at the high end.

## Slide 8: Passenger Car Age Distribution Results
Source Type | Pollutant | Case | Average Age | Emission Rate (gram/vehicle-mile) | Percent Change
Passenger Car | CO | Baseline | 7.48 | 1.484 | -
 |  | Scenario 1 | 7.68 | 1.516 | 2.15%
 |  | Scenario 2 | 7.86 | 1.548 | 4.14%
 |  | Scenario 3 | 8.21 | 1.604 | 7.49%
 |  | Scenario 4 | 8.53 | 1.653 | 10.24%
 |  | Scenario 5 | 9.24 | 1.776 | 16.47%
 | NOX | Baseline | 7.48 | 0.2929 | -
 |  | Scenario 1 | 7.68 | 0.3017 | 2.91%
 |  | Scenario 2 | 7.86 | 0.3104 | 5.63%
 |  | Scenario 3 | 8.21 | 0.3246 | 9.76%
 |  | Scenario 4 | 8.53 | 0.3367 | 12.99%
 |  | Scenario 5 | 9.24 | 0.3700 | 20.84%
 | VOC | Baseline | 7.48 | 0.0398 | -
 |  | Scenario 1 | 7.68 | 0.0409 | 2.88%
 |  | Scenario 2 | 7.86 | 0.0421 | 5.56%
 |  | Scenario 3 | 8.21 | 0.0439 | 9.51%
 |  | Scenario 4 | 8.53 | 0.0455 | 12.62%
 |  | Scenario 5 | 9.24 | 0.0502 | 20.78%
 | PM2.5 | Baseline | 7.48 | 0.0067 | -
 |  | Scenario 1 | 7.68 | 0.0068 | 1.16%
 |  | Scenario 2 | 7.86 | 0.0069 | 2.27%
 |  | Scenario 3 | 8.21 | 0.0070 | 4.01%
 |  | Scenario 4 | 8.53 | 0.0071 | 5.56%
 |  | Scenario 5 | 9.24 | 0.0075 | 9.94%
Notes: Shows that the emissions rates increase as the fleet gets older and more vairable.
Once again highlight that these ranges are observed from an actual MPO. Shows how much the fleet can change for the same area in just a few years.
Also, highlight that is shows how important it is to get the most recent age distribution. For certain analyses it may be important to forecast possible aging of the fleet.

## Slide 9: Fleet Mix
Analyzed five cases to determine how sensitive fleet can be a specific MOVES link
The five cases include
  Geographic area comparisons of fleet mix(Georgia Tech provided data)
  Passenger Car to Passenger Truck ratio
  Percent Truck Mix
  Truck Type Mix
  Transit Bus Mix
Notes: We will only show the passenger Car to Passenger Truck Ratio Case.
Mentioned Ga. Tech for the Geographic area case.

## Slide 10: Passenger Car to Passenger Truck Ratio
Passengers Car and Passenger Truck CO emission rates are significantly different
This analysis tested how sensitive this ratio is and the impact on emission rates from MOVES
Notes: First Bullet: Passenger Trucks are much higher than passenger cars in MOVES.

## Slide 11: Passenger Car to Passenger Truck Ratio Results
Pollutant | Description | Emission Rate (gram/vehicle-mile) | Percent Change
CO | Baseline_Highway | 2.5700 | -
 | Passenger Cars +5%/Passenger Trucks -5% | 2.4692 | -3.92%
 | Passenger Cars +10%/Passenger Trucks -10% | 2.3684 | -7.84%
 | Passenger Cars +20%/Passenger Trucks -20% | 2.1668 | -15.69%
 | Passenger Cars -5%/Passenger Trucks +5% | 2.6708 | 3.92%
 | Passenger Cars -10%/Passenger Trucks +10% | 2.7716 | 7.84%
 | Passenger Cars -20%/Passenger Trucks +20% | 2.9733 | 15.69%
NOX | Baseline_Highway | 1.2006 | -
 | Passenger Cars +5%/Passenger Trucks -5% | 1.1727 | -2.33%
 | Passenger Cars +10%/Passenger Trucks -10% | 1.1447 | -4.65%
 | Passenger Cars +20%/Passenger Trucks -20% | 1.0889 | -9.31%
 | Passenger Cars -5%/Passenger Trucks +5% | 1.2285 | 2.33%
 | Passenger Cars -10%/Passenger Trucks +10% | 1.2565 | 4.65%
 | Passenger Cars -20%/Passenger Trucks +20% | 1.3123 | 9.31%
Notes: The closer you are to a 50/50 split the higher the CO and NOX rates will be.
The main take away is that if you can increase your proportion of passenger trucks your CO and NOX rates can go up by a significant amount.
It will be important to classify these vehicles appropriately.

## Slide 12: Average Speed and Operating Mode Distribution Comparison
Compared utilizing average speed for a link to a user defined operating mode distribution
  When using average speed with MOVES, default drive schedules are applied
Highway Capacity Manual (HCM) based drive schedules
Georgia Tech provided operating mode distributions
Notes: During the first main and sub bullet explain the how the average speed works and the different options that can be used.
Average Speed
Drive Schedule
Operating Mode Distribution. Remind everyone that everything turns into an operating mode distribution.
Mention Ga. Tech here again and how important they were for this portion of the analysis.

## Slide 13: Example of MOVES Default Drive Schedules
Notes: Explain that the default drive schedules might not represent the type of link we are tying to model
1029 – Red line in the chart – represents an average speed of 31.02 mph. There are speeds all the way up to 64-65 mph in the drive schedule. This might not represent an arterial you want to model.

## Slide 14: Intersection Analysis
Intersection
  25 mph, 35 mph, 45 mph approach speeds
  LOS B,D, and E
  Consisted of approach, queue, and departure (acceleration) links
Approach Speed (mph) | LOS | Signal Cycle Length (seconds) | Yellow Time (seconds) | Green Time (seconds) | Red Time (seconds) | Vehicle Headway (seconds) | Decel Rate (mph/s) | Acc Rate (mph/s) | Volume per Cycle
35 | B | 55 | 4 | 10 | 41 | 14 | -5 | 3 | 4
 | D | 95 | 4 | 23 | 68 | 10 |  |  | 10
 | E | 95 | 4 | 23 | 68 | 9 |  |  | 11
35 mph Scenario Intersection Data
Notes: This is an example of the detail we come up with to develop these scenarios.
We used this information in conjunction with the kinematic equations.
We developed our own drive schedules and using the VSP calculation converted them into Operating Mode Distributions.

## Slide 15: Operating Mode Distributions
35 mph Intersection Scenario – Queue Links LOS D Operating Mode Distributions
Notes: For the Queue link LOS D in the 35 mph scenario
Blue is MOVES average speed
Red is HCM generated
Green is Georgia Tech provided.

## Slide 16: Intersection Results
Link Description | LinkID | Modeled Average Speed (mph) | Level of Service | CO Emission Rate (gram/veh-mile) | CO % Difference Compared to Average Speed | NOX Emission Rate (gram/veh-mile) | NOX % Difference Compared to Average Speed
Intersection Queue Link Average Speed | 111 | 15.94 | LOS B | 3.066 | - | 0.366 | -
Intersection Queue Link HCM | 11 |  |  | 1.858 | -39.38% | 0.2254 | -38.41%
Intersection Queue Link GATech | 211 |  |  | 1.53 | -50.09% | 0.1875 | -48.77%
Intersection Queue Link Average Speed | 114 | 13.04 | LOS D | 3.273 | - | 0.3754 | -
Intersection Queue Link HCM | 14 |  |  | 2.477 | -24.32% | 0.3274 | -12.77%
Intersection Queue Link GATech | 214 |  |  | 1.871 | -42.85% | 0.2292 | -38.95%
Intersection Queue Link Average Speed | 117 | 13.81 | LOS E | 3.209 | - | 0.3725 | -
Intersection Queue Link HCM | 17 |  |  | 2.391 | -25.49% | 0.3144 | -15.59%
Intersection Queue Link GATech | 217 |  |  | 1.766 | -44.97% | 0.2164 | -41.91%
Notes: Large variations compared to average speed for the queue segment.
CO and NOX results.
Very important finding for getting a good representative operating mode distribution for the segment being modeled.

## Slide 17: Some of the Findings
Variations in Age Distribution from year to year can impact emission rates
Passenger Car to Passenger Truck Ratio is important
The proportion of combination trucks in your fleet mix has a large influence on composite emission rates
Although a small sample size from this analysis:
  There is large variation in emissions rates when comparing average speed to the HCM based operating mode distribution and/or Georgia Tech operating mode distribution.
Notes: Tell them more are highlighted in the report.

## Slide 18: Acknowledgments
Michael Claggett and Paul Heishman from FHWA
Ann Xu, Randy Guensler, and Vetri Elango from Georgia Tech
The late Ron Kirby from the Metropolitan Washington Council of Governments (MWCOG)

## Slide 19: Questions?