## Slide 1
A Simple Approach for the Auralization of Moving Sources
Aaron Hastings
The National Transportation Systems Center
Advancing transportation innovation for the public good
U.S. Department of Transportation
Office of the Secretary of Transportation
John A. Volpe National Transportation Systems Center
Inter-Noise 2015

## Slide 2: Background
Needs
  Sound Signal Development – Human Response Testing
  Soundscape Simulation – Community Outreach
Software to Auralize Moving Sources
  Commercial / Proprietary
  Source / Environment Specific
  Optimized for Speed
Method Requirements
  Signal and Processing Agnostic
  Modifiable / Extensible
  Open / Transparent Implementation
  Near Real-time
  Batch Processing
In Situ Testing: Time, Expense, Accuracy
Notes: Needs
  Sound Signal Development – Human Response Testing (performance, annoyance, etc.)
  Soundscape Simulation – Community Outreach
Software to Auralize Moving Sources
  Commercial / Proprietary ( Research: DIVA at the Helsinki University of Technology, RAVEN at Aachen University. Commercial: B&K. Gaming: Unity, Blender)
  Application Specific (Game Development, Architectural, Research Tools for Specific Sound Environments)
Approach Requirements
  Signal and Processing Agnostic
  Modifiable / Extensible
  Open / Transparent Implementation
  Near Realtime
  Batch Processing

## Slide 3: Assumptions
Point Source in Far Field
Ray Acoustics
Homogeneous Atmosphere
Free Field Propagation
  No reflections, edge diffractions, etc
  Add hard ground using image sources
Receiver & Source:
  Translate in X, Y, Z
  Rotate horizontally (azimuth) & vertically (elevation)
Receiver
  Translation removed after source defined
source
receiver
Image source
Notes: Current focus is handling moving sources
Future focus on advancing propagation modeling

## Slide 4: Implementation
Matlab Main Function
Sub-routines
  Allow Switching Methodologies
  May Require Additional Assumptions
Sub-routines:
  Define Receiver
  Define Source
  Define Signal at Source
  Determine Time Delay for Propagation
  Determine Attenuation (Divergence, Atmospheric Absorption)
  Adjust for Signal Directivity
  Adjust for Receiver Head Related Transfer Functions (HRTFs)
  Output Signal
Notes: Modular implementation

## Slide 5: Defining Receiver and Source
Flat Earth X, Y, Z (RHR)
Horizontal (Azimuth) Angle
Vertical (Elevation) Angle
Receiver Defined First
Receiver Translation Removed during Source Definition
  Subtract Receiver Translation Vector from Source Translation Vector
  Receiver and Source Angles Computed after Receiver Translation Removed
Final Distances and Angles Defined for Fix Reference Frame Centered on Receiver

## Slide 6: Defining Signal
Signal can be Defined Using:
  Stationary time signal
  Parametric formulae
  Sinusoids and band-limited noise
Propagation from Source to Receiver:
  Time Delay  Produces Doppler Shift
  Non-uniform time intervals at receiver
  Interpolation used to generate uniform time at receiver
Interpolation:
  Nearest Neighbor
  Linear
  Spline
  Lagrange
  Whittaker-Shannon
  Lanczos
Doppler Shift Obtained Here
Uniform Time Sample
Recovered, Preserving
Doppler Shift
Notes: Reference: Non-Uniform Sampling in Statistical Signal Processing -- Frida Eng
Assuming low speeds relative to C
Interpolation: Uniform or non-uniform, periodic or aperiodic
Lantsohsh

## Slide 7: Free-field Attenuation
Divergence – 6 dB / doubling
Atmospheric Absorption: ISO 9613-1
  Function of Frequency and Distance
  Frequency Associated w/. Time Interval
  Distance Associated w/. Single Sample
  Approach:
    Develop Filters for Each 3 dB of Overall Attenuation
    Linear Interpolation: Weighted average of two nearest distances for each sample
Frequency (Hz) | Attenuation (dB/m) | Frequency (Hz) | Attenuation (dB/m)
50 | 7.81E-05 | 800 | 3.91E-03
63 | 1.22E-04 | 1000 | 4.66E-03
80 | 1.94E-04 | 1250 | 5.71E-03
100 | 2.94E-04 | 1600 | 7.45E-03
125 | 4.40E-04 | 2000 | 9.89E-03
160 | 6.71E-04 | 2500 | 1.36E-02
200 | 9.54E-04 | 3150 | 1.97E-02
250 | 1.31E-03 | 4000 | 2.97E-02
315 | 1.74E-03 | 5000 | 4.42E-02
400 | 2.24E-03 | 6300 | 6.76E-02
500 | 2.73E-03 | 8000 | 1.05E-01
630 | 3.27E-03 | 10000 | 1.59E-01
Notes: Sums to 1 if hnear = hfar

## Slide 8: Adjusting for Directivity and HRTFs
Measured HRTFs
  Center for Image Processing and Integrated Computing (CIPIC) at U.C. Davis
  Azimuth Angles: +/- 80, 65, 55, 45, 40, 35, 30, 25, 20, 15, 10, 5, 0 deg
  Elevation Angles: : -45 to 230.625 deg (5.625 degree increments)
  Angles Relative to Head Orientation
Directivity
  Uses Monopole unless directivity provided
  Same format as for HRTFs
  Angles based on Fixed Reference Frame (Independent of Head Rotation)
Interpolation
  Similar to that used for Atmospheric Absorption
  Except nearest neighbors determined for azimuth and elevation: Bilinear Interpolation
Notes: Note in paper just used a linear interpolation weighting applied to both, simpler, but a rougher estimate. Bilinear is better.

## Slide 9: Sample Results
Spectrogram of 440 Hz pure tone source signal passing by receiver at 8.33 m/s with perpendicular distance of 10 m. No head-related transfer function or source directivity is applied.
Notes: Bigger fonts, () for sec

## Slide 10: Sample Results
Spectrogram of 440 Hz pure tone source signal passing by receiver at 8.33 m/s with a perpendicular distance of 10 m. Head-related transfer function applied by using a weighted interpolation.

## Slide 11: Next Steps
Extend Functionality to Include Reflections (e.g. Ground Effects) and Edge Diffractions (e.g. Shielding)
Improve Interpolation Functions
Add HRTFs with Higher Spatial Resolution
Add Dipole, Cardioid, etc. Directivity Patterns
Add other Atmospheric Absorption Standards
Develop Library of Standard Sound Sources
Develop Library of Standard Source Trajectories
Add Metric Computations and Calibrations for Signal at Source and at Receiver

## Slide 12: Questions / Comments?
Aaron.Hastings@dot.gov