## Slide 1: ODOA Test Result & Analysis
Perrone Robotics
2025 August
Bus Wash #7 TEST: 2025-06-11_11.51.03

## Slide 2
Event Summary
Perrone Robotics
2025 August
Vehicle State at detection
Cycle: 1995
Speed: 0.99mph
Heading: 32.4
Collision Detection Details:
Detection Type: Lane Collisions
Object width: 1.95
Object Distance: 1.58m
Observations:
During LiDAR monitoring at Cycle 1995, a potential lane collision point was detected while the vehicle was still moving. The system flagged a possible object within the lane path which can be identified as the wall from the exit of the tunnel.

## Slide 3
Legend:
Pink cross: Vehicle’s location
Yellow lines: collision point path
Yellow circled cross: Object detected
Dotted white line: Vehicle’s path

## Slide 4
Bus
Exit of the tunnel