## Slide 1: ODOA Test Result & Analysis
Perrone Robotics
2025 August
Intersections #7 TEST: 2025-06-11_14.51.36

## Slide 2
Event Summary
Perrone Robotics
2025 August
During LiDAR monitoring at Cycle 254, a potential lane collision point was detected while the vehicle was still moving. The system flagged a possible object within the lane path.
Vehicle State at detection
Cycle: 254
Speed: 7.07mph
Heading: 119.9
Collision Detection Details:
Detection Type: Obstacle collision
Object width: N/A
Object Distance: 8.32m
Observations:
In this test, the bus is observed waiting to make a left turn across opposing traffic, proceeding only when the path is clear. It reaches a maximum speed of 7.07 mph before decelerating, prompted by both the initiation of the turn and the detection of an object 8.32 m ahead. Additionally, vehicles approaching from the opposite direction of the left turn can be seen in the following slide, represented by yellow lines with a yellow circled cross at the end. This opposing traffic is also a contributing factor to the bus’s reduction in speed prior to completing the turn.

## Slide 3
Legend:
Pink cross: Vehicle’s location
Yellow lines: collision point path
Yellow circled cross: Object detected
Dotted white line: Vehicle’s path