## Slide 1
Event Summary - ODOA #63 03-20-2025_19-00-18_RC Pedestrian on Right
During LiDAR monitoring at Cycle 281, a potential lane collision point was detected while the vehicle was nearly stationary. The system flagged a possible object within the lane path.
Vehicle State at Detection
Cycle: 281
Speed: 0.02 mph (vehicle coming to a stop)
Heading: 212.7°
Latitude: 30.375807°
Longitude: -97.724684°
Collision Detection Details
Detection Type: Lane collision candidate
Object Width: 0.39 m
Object Distance from Vehicle (front bumper reference): 1.79 m
Lane Lateral Offset (Left): 29.12 m
Lane Lateral Offset (Right): 1.75 m
Observations
The detected object is small (less than half a meter wide) and positioned close to the vehicle’s right side within the projected lane boundaries.
Given the vehicle’s extremely low speed, this detection likely occurred during final deceleration or while idling at a stop.
The detection lies well within the ~2 m forward danger zone, indicating a high-priority obstacle if movement resumes without clearance.

## Slide 3
On March 20, 2025, at 19:00:18 (Cycle 281), the vehicle’s LiDAR system was tracking a previously detected potential lane collision point. The initial detection occurred prior to this cycle, prompting the vehicle to begin decelerating. By Cycle 281, the vehicle’s speed had reduced to 0.02 mph, effectively coming to a stop, with a heading of 212.7 degrees. The logged GPS position at this time was latitude 30.375807° and longitude -97.724684°.
The object identified by LiDAR measured approximately 0.39 meters in width and was located 1.79 meters ahead of the vehicle’s reference point (pink cross). Lane offset measurements placed the object 29.12 meters from the left lane boundary and 1.75 meters from the right lane boundary, situating it directly within the projected travel path.
Because of its proximity—well within the two-meter forward danger zone—the object represented a high-priority obstacle that warranted a stop.
Event Summary

## Slide 4: LiDAR Obstacle Detection Report – Raw Sensor View
Speed: 0.02 mph (decelerating to stop)
Heading: 212.7°
GPS Position: Latitude 30.375807°, Longitude -97.724684°
Sensor View Analysis: The raw LiDAR visualization confirms the detection of a potential collision object in the vehicle’s path. In this view:
Green dots: Represent the vehicle’s projected path.
Blue circular lines: Represent ground contact points from LiDAR returns.
Two large overlapping red rectangles: Indicate fixed bike rack structures.
Smaller forward red rectangle: Marks the exact detection point of the potential collision object.
Within the smaller red rectangle, a faint, light-blue dot outline of a human figure is visible, confirming the object was a pedestrian.
Detection Summary: The object (pedestrian) was initially detected before Cycle 281, triggering the vehicle’s collision-avoidance system and causing it to slow significantly. By the time of this snapshot, the pedestrian was located approximately 1.79 meters ahead of the vehicle and directly within its path, between the left and right lane boundaries.
Event Summary

## Slide 6
The vehicle’s LiDAR sensors confirmed the presence of a pedestrian in its direct path.
The detection occurred prior to Cycle 281, which led the vehicle to decelerate to a near stop—recorded at 0.02 mph with a heading of 212.7 degrees at the time of capture. The raw sensor visualization shows the green dots marking the planned travel path, blue concentric lines indicating ground LiDAR contact points, and two large overlapping red rectangles corresponding to stationary bike racks.
Ahead of these, a smaller red rectangle marks the collision detection point. Within this smaller rectangle, a faint light-blue dot outline reveals the figure of a person, verifying that the object was a pedestrian.
The pedestrian was positioned approximately 1.79 meters ahead, directly within the projected lane, prompting the vehicle’s collision-avoidance system to halt forward motion.
Event Summary

## Slide 7
From this alternate angle, the overlapping red rectangles marking the bike racks are clearly visible, along with the faint dotted outline of the pedestrian on the vehicle’s right side.