## Slide 1: ODOA Test Result & Analysis
Perrone Robotics
2025 August
ODOA #64 TEST: 03-20-2025_19-10-27

## Slide 2
Event Summary
Perrone Robotics
2025 August
During LiDAR monitoring at Cycle 222, a potential lane collision point was detected while the vehicle was still moving. The system flagged a possible object within the lane path.
Vehicle State at detection
Cycle: 222
Speed: 7.46mph
Heading: 122
Collision Detection Details:
Detection Type: Lane collision
Object width: 0.63m
Object Distance: 2.92m
Observations:
Object detected by the vehicle’s LiDAR is small (less than half a meter wide and positioned close to the vehicle’s left side within the projected lane boundaries.
The detection lies closely within the 2m danger zone, indicating a high-priority obstacle if movement resumes without clearance.

## Slide 3
Legend:
Pink cross: Vehicle’s location
Yellow lines: collision point path
Yellow circled cross: Object detected
Dotted white line: Vehicle’s path

## Slide 4
During LiDAR monitoring at Cycle 222, a potential lane collision point was detected while the vehicle was still moving. The system flagged a possible object within the lane path.
Object Detected.
Bus bike rack

## Slide 5
Event Summary
Perrone Robotics
2025 August
A few moments later, the same identified object was closer still to the bus, thus prompting the vehicle to a stop.
Vehicle State at detection
Cycle: 599
Speed: 0.01mph
Heading: 122.9
Collision Detection Details:
Detection Type: Lane collision
Object width: 4.84m
Object Distance: 6.06m
Observations:
Object detected by the vehicle’s LiDAR is extremely close to the vehicle left side and within the projected lane boundaries. Indicating a high-priority obstacle if movement resumes without clearance, thus causing the vehicle to stop.

## Slide 6
Legend:
Pink cross: Vehicle’s location
Yellow lines: collision point path
Yellow circled cross: Object detected
Dotted white line: Vehicle’s path

## Slide 7
Object Detected.
Bus bike rack