## Slide 1: ODOA Test Result & Analysis
Perrone Robotics
2025 August
ODOA #66 TEST: 2025-03-20_19.23.26

## Slide 2
Event Summary
Perrone Robotics
2025 August
During LiDAR monitoring at Cycle 184, a potential lane collision point was detected while the vehicle was still moving. The system flagged a possible object within the lane path.
Vehicle State at detection
Cycle: 184
Speed: 5.34mph
Heading: 31.2
Collision Detection Details:
Detection Type: Obstacle collision
Object width: N/A
Object Distance: 79.37m
Observations:
The object detected by the vehicle’s LiDAR was registered as small, a consequence of both its distance and the system’s inability, at the moment of data acquisition, to resolve its actual dimensions—resulting in a recorded width of “0 m”—yet nonetheless triggering a collision warning due to its proximity to the vehicle’s projected path.

## Slide 3
Legend:
Pink cross: Vehicle’s location
Yellow lines: collision point path
Yellow circled cross: Object detected
Dotted white line: Vehicle’s path

## Slide 4
During LiDAR monitoring at Cycle 184, a potential lane collision point was detected while the vehicle was still moving. The system flagged a possible object within the lane path.
Object Detected.
Bus bike rack

## Slide 5
Event Summary
Perrone Robotics
2025 August
A few moments later, another object was identified by the system, thus prompting the vehicle to a stop.
Vehicle State at detection
Cycle: 229
Speed: 5.03mph
Heading: 32.6
Collision Detection Details:
Detection Type: Obstacle detection
Object width: 2.41m
Object Distance: 6.06m
Observations:
Object detected by the vehicle’s LiDAR is extremely close to the vehicle left side and within the projected lane boundaries. Indicating a high-priority obstacle if movement resumes without clearance, thus causing the vehicle to stop.

## Slide 6
Legend:
Pink cross: Vehicle’s location
Yellow lines: collision point path
Yellow circled cross: Object detected
Dotted white line: Vehicle’s path

## Slide 7
Object Detected.
Bus bike rack