## Slide 1: ODOA Test Result & Analysis
Perrone Robotics
2025 August
ODOA #67 TEST: 2025-03-20_19.26.35

## Slide 2
Event Summary
Perrone Robotics
2025 August
During LiDAR monitoring at Cycle 202, a potential lane collision point was detected while the vehicle was still moving. The system flagged a possible object within the lane path.
Vehicle State at detection
Cycle: 202
Speed: 3.2mph
Heading: 32.5
Collision Detection Details:
Detection Type: Obstacle Detections
Object width: 0.43
Object Distance: 2.55m
Observations:
The object detected by the vehicle’s LiDAR was positioned on the right side in immediate proximity to the vehicle, sufficiently near its projected driving path to prompt the system to initiate a full stop.

## Slide 3
Legend:
Pink cross: Vehicle’s location
Yellow lines: collision point path
Yellow circled cross: Object detected
Dotted white line: Vehicle’s path

## Slide 4
Object Detected.
Bus bike rack

## Slide 5
Event Summary
Perrone Robotics
2025 August
A few moments later, the same object identified prompted the vehicle to come to a complete stop.
Vehicle State at detection
Cycle: 289
Speed: 0.01mph
Heading: 32.2
Collision Detection Details:
Detection Type: Obstacle detection
Object width: 0m
Object Distance: 4.65m
Observations:
Object detected by the vehicle’s LiDAR is extremely close to the vehicle right side and within the projected lane boundaries. Indicating a high-priority obstacle if movement resumes without clearance, thus causing the vehicle to stop.

## Slide 6
Legend:
Pink cross: Vehicle’s location
Yellow lines: collision point path
Yellow circled cross: Object detected
Dotted white line: Vehicle’s path
Object Detected. (Human)