## Slide 1: Factors of the Precast Concrete Supply Chain: An Interpretive Structural Modeling Approach
By
Anik Mazumder and Bhaba R. Sarker
Louisiana State University
amazum3@lsu.edu ● (225) 220-2006
bsarker@lsu.edu ● (225) 578-5370
Graduate Research Conference, LSU Student Union, LSU, Baton Rouge, LA (April 30, 2024)
Acknowledgment: This project is fully funded by TRANSPORTATION INFRASTRUCTURE PRECAST INNOVATION CENTER (TRANS-IPIC) #LS-23-RP-04

## Slide 2
Introduction
Precast Concrete
Cast in reusable molds/form
Cured in a controlled setting.
Transported and installed at the site.
Advantages of Precast Concrete
Uniform quality with controlled manufacturing.
Faster erection and reduced project times.
Long-lasting with minimal maintenance.
Less site disturbance.
Flexible in design, shapes, and finishes.

## Slide 3
Background
Precast concrete users and manufacturers should recognize that the main reasons for low utilization of precast concrete systems predominantly depend on the prevailing conditions of the country in question (Polat, 2010).
Practitioners should be well informed about the factors that affect the use of precast concrete systems if these systems are to be used more extensively (Polat, 2008).
There is a major shortage of expert personnel capable of designing and organizing projects involving precast concrete systems and that almost half the contractors surveyed did not observe significant factors when they used precast concrete systems (Arditi et al., 2000).
Moreover, identifying the critical factors can provide a reference for practitioners to carry out quality management in assembly construction (Xia et al., 2021).

## Slide 4
Motivation
Research Gap
Lack of research in consideration of factors related to cost, reliability, and sustainability of Precast Concrete and optimization of its logistics.
Research gap in finding interdependencies among factors affecting precast concrete supply systems.

## Slide 5
Objective
To Develop a Hierarchy Framework of Significant Factors Representing their Interdependencies of Precast Concrete Supply System using Interpretive Structural Modelling
Identifying Factors
Factors associated with Cost, Reliability and Sustainability
Exploring Interdependencies
Contextual Relationships in each elements
Developing Hierarchical Diagraph
Helpful to Develop an Optimal Supply Chain Model for Precast Operations.

## Slide 6
Method
Interpretive Structural Modelling (ISM):
Used for Theory Building
Helps to identify and define the variables, the relationship between them
Steps to Perform ISM:
Identification and defining of elements
Establishing contextual relationship between elements
Reachability Matrix and Transitivity Check
Partition of the final reachability matrix
Developing Diagraph (Menon and Suresh, 2020)

## Slide 7
Develop a Structural Self-Interaction Matrix
Develop an Initial Reachability Matrix
Test Matrix for Transitivity Rule
Clustering the Factors
Level Partitioning
Satisfied
Not
Satisfied
Methodology
List of Some Significant Factors Associated with Cost-effectivity, Reliability and Sustainability
Draw the Hierarchy Framework of Significant Factors of PC Supply System

## Slide 8
Factors (Total 18)

## Slide 9
Structural Self-Interaction Matrix (SSIM)
V = Relation from element i to element j (not in reverse)
A = Relation from element j to element i (not in reverse)
X = Relations in both the directions
0 = No valid relation

## Slide 10
Reachability Matrix
Following steps were for this conversion,
If = V, then = 1 and = 0
If = A, then = 0 and = 1
If = X, then = = 1
If = 0, then = = 0
SSIM, = []
Reachability Matrix, = []
A matrix that captures the reachability requirements. Each row/column of the matrix denotes a network, and each cell specifies whether the element of the row can reach the element of the column.

## Slide 11
Final Reachability Matrix
Initial Reachability Matrix
Final Reachability Matrix
Transitivity Check
Hardness of Cement Paste (HCP)
Water Cement Ratio (w/c)
Cement Content (CC)
Transitive Relation

## Slide 12
Factors | QC | PV | TIQ | RMRUR | MTBF | FDD | ARTTS | CC | AS | W/C | COR | TPC | SPC | PDEPC | HCP | SCP | A&R | CCR | Driving Power
QC | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 9
PV | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 4
TIQ | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 3
RMRUR | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 3
MTBF | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3
FDD | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2
ARTTS | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
CC | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 4
AS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 3
W/C | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 5
COR | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 2
TPC | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 3
SPC | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 3
PDEPC | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 2
HCP | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 5
SCP | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 5
A&R | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 4
CCR | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
Dependence Power | 1 | 2 | 3 | 2 | 3 | 2 | 3 | 5 | 2 | 6 | 2 | 3 | 3 | 2 | 6 | 7 | 3 | 7 | 62
Final Reachability Matrix

## Slide 13
Level Partitions
An iterative that requires the comparison between the reachability set and the antecedents set.
The reachability set includes the factor in question along with all factors affected by it.
The antecedent set comprises the factor and all factors influencing it.
The intersection of these sets is derived for all the factors and levels of different factors are determined.
The factors for which the reachability and the intersection sets are the same occupy the top level in the hierarchy (Attri et al., 2013).
Notes: After developing the final reachability matrix, the level partition process was carried out to know the placement of elements of factors level wise.

## Slide 14
Serial | Factors | Antecedent Sets | Reachability Sets | Intersection Sets | Level
1 | QC | 1,8-11,15-18 | 1 | 1 | 
2 | PV | 2,4-5,14 | 2,14 | 2,14 | 1
3 | TIQ | 3,12,13 | 3,12,13 | 3,12,13 | 
4 | RMRUR | 4,5,15 | 2,4 | 4 | 
5 | MTBF | 5-7 | 2,4,5 | 5 | 
6 | FDD | 6,7 | 5,6 | 6 | 
7 | ARTTS | 7 | 5-7 | 7 | 1
8 | CC | 8,10,15,16 | 1,8,10,15,16 | 8,10,15,16 | 1
9 | AS | 9,16,17 | 1,9 | 9 | 
10 | W/C | 8,10,15,16,18 | 1,8,10,15,16,17 | 8,10,15,16 | 
11 | COR | 11,18 | 1,11 | 11 | 
12 | TPC | 3,12,13 | 3,12,13 | 3,12,13 | 1
13 | SPC | 3,12,13 | 3,12,13 | 3,12,13 | 1
14 | PDEPC | 2,14 | 2,14 | 2,14 | 1
15 | HCP | 8,10,15,16,18 | 1,4,8,10,15,16 | 10,15,16 | 
16 | SCP | 8,10,15,16,18 | 1,8-10,15-17 | 8,10,15,16 | 
17 | A&R | 10,16-18 | 1,9,17 | 17 | 
18 | CCR | 18 | 1,10,11,15-18 | 18 | 1
Level Partitions (For Level 1)

## Slide 15
Level Partitions
Leveling all the factors helped to develop the diagraph which would provide representation of all the factors and their hierarchical relationships with the other factors.
The factors having the lowest number of level are those factors that will not lead the other factors above their own level in the hierarchy.
The factors having the highest number of level will depend on various factors above their own hierarchical levels.

## Slide 16
Hierarchical Diagraph of Factors

## Slide 17
Dashed lines denote transitive relationships among the factors, while solid arrows indicate direct links.
A factor positioned at an elevated level signifies its capacity to impact a greater number of other factors (Yadav and Samuel, 2022).
For example, if we take QC, we can identify the factors on which QC is highly dependent such as CC (Cement Content), W/C (Water-cement ratio), CCR (Chloride and Carbonation Resistance) etc.
Result Discussion

## Slide 18
Conclusion and Future Work
All the identified factors will help to build up the optimal supply system with the minimization of precast concrete supply system’s cost and improvement of reliability and sustainability of precast concrete.
Using these interdependencies, a mathematical model will be developed to consider the price volatility and uncertainty of materials to improve supply logistics of precast concrete.

## Slide 19
References
Arditi, D., Ergin, U., & Günhan, S. (2000). Factors affecting the use of precast concrete systems. Journal of architectural engineering, 6(3), 79-86.
Polat, G. (2008). Factors affecting the use of precast concrete systems in the United States. Journal of Construction Engineering and Management, 134(3), 169-178.
Sarker, B. R. (2024), “Developing A Cost-Effective, Reliable, and Sustainable Precast Supply System under Price Volatility and Uncertainty of Material Supply. A report submitted to the DOT/Trans-IPIC, Grant #LS-23-RP-04 (for first quarter, January 1-March 31, 2024).
Sarker, B.R. (2023), “Developing A Cost-Effective, Reliable, and Sustainable Precast Supply System under Price Volatility and Uncertainty of Material Supply,” A proposal submitted to the DOT/Trans-IPIC, Grant #LS-23-RP-04.
Sarker, B. R. and Baylot, E. A. (2012), “Throughput capacity estimation for convoy movement in linked roads,” ASCE-Journal of Transportation Engineering, September 2012; 138(9): pp. 1133-1142.
Sarker, B. R., Baylot, E. A., Green, J. G, and Biswas, P. (2012), “Convoy movement: consideration of turning geometrics for selected vehicle shapes,” ASCE-Journal of Transportation Engineering, May 2012, 138 (5): pp. 502-511.
Sushil. (2012), “Interpreting the interpretive structural model,” Global Journal of Flexible Systems Management, 13(2), 87–106. https://doi.org/10.1007/S40171-012-0008-3.
Warfield, J. N. (1974), “Developing Interconnection Matrices in Structural Modeling,” IEEE Transactions on Systems, Man and Cybernetics, SMC-4(1), 81–87. https://doi.org/10.1109/TSMC.1974.5408524.
Xia, M., Zhao, L., Qiao, Y., Yuan, Z., Cui, Y., Zhao, L., & Li, J. (2022). Analysis of factors affecting the quality of precast components based on structural equation modeling. Arabian Journal for Science and Engineering, 1-15.
Yadav, A. K., and Samuel, C. (2022). Modeling resilient factors of the supply chain. Journal of Modelling in Management, 17(2), 456–485. https://doi.org/10.1108/JM2-07-2020-0196.

## Slide 20
Thank you.
Any Question?