## Slide 1
Optimizing Pallet Capacity Utilization to Minimize Curing Cost in Precast Concrete Manufacturing
TRANS-IPIC Research Webinar: July 22, 2024
By
Anik Mazumder
and
Bhaba R Sarker
Department of Mechanical and Industrial Engineering
3261 Patrick F. Taylor Hall
Louisiana State University
Baton Rouge, LA 70803
E-mail: bsarker@lsu.edu (Sarker) and Phone: +1 (225) 578-5370
E-Mail: amazum3@lsu.edu (Mazumder) and Phone: +1 (225) 220-2006

## Slide 2
Outline
Introduction
What is the Existing Problem
Model Development
An Illustrative Example
Computational Results
Computational Performance
Future Work
Application and Scope
Working Papers
References

## Slide 3
1. Introduction
Precast Concrete (PC)
Refers to concrete components that are molded and cured in a controlled factory environment before being transported to a construction site.
Example: Bridge beams, pavement slabs, etc.
Benefits
Consistent Quality
Corrective plan and design
Efficient Installation
Accelerated Construction Process

## Slide 4
Motivation
Importance of Efficient PC Production
Transportation Infrastructure:
Roads, Bridges, Urban Transit Systems
Essential for economic growth and connectivity.
Timeliness and Cost-Effectiveness
  Critical for maintaining project schedules and budgets.
*Tayabji et al. (2010)
*Courtesy: HOUSING.com

## Slide 5
Motivation
Importance of Efficient PC Production
Production Challenges:
Mold setting and Curing process
Significant impact on cost and efficiency.
Resource Intensive
  High energy and labor cost.
Inefficient use of pallet space
PC products
Kiln Chamber

## Slide 6
Literature Review
Several studies have addressed various computational techniques that have aimed to address planning issues and, to reduce costs and project completion times
Findings | Authors
Proposed heuristic for job scheduling. | (Dawood, 1995)
Developed genetic algorithm for flow-shop sequencing. | (Chan and Hu, 2002)
Proposed an integer linear programming model, To schedule the production of beams To minimize the empty spaces in the molds. | (Prata et al., 2015)
Developed a heuristic method Solve a sub-optimal model for Configured pallet layout during curing operations. | (Wang et al., 2018)

## Slide 7
Research Gap
1. Specific Production Process
Limited focus on optimizing specific production processes such as,
2. Dynamic Manufacturing Environments
Traditional models often assume
How the components will be arranged in a batch or pallet for being cured
How many batches or pallets will be required
Static conditions,
No variability in demand and deadlines

## Slide 8
2. What is the Existing Problem
A single component is placed in a batch in the curing chamber.
A higher number of batches or cycles
Delivery deadlines are missed and extra penalties
Optimal strategy for placement of curing materials or components

## Slide 9
Need for Current Study
Research Goal
To minimize the curing cost by maximizing the average utilization of pallet capacity.
Research Objective
To develop a new plan
For optimal layout configuration to arrange PC components on pallets
To minimize batch or pallet cycles during the curing process

## Slide 10
3. Model Development
The formulation of the Curing Cost Minimization (CCM) model will be shown using some standard notations.
(a) Indices
= Type of component ( = 1, 2, …, m)
= Precast layout on a pallet, ( = 1, 2, …, n)
(b) System Constants
= Batch size (Maximum number of pallets that can be cured per batch (pallets/batch)
= Unit cost of energy (dollars/kWh)
= Labor cost for loading and unloading components on the pallet ($/hours)
= Demand of component type (components)
= Energy consumption rate for curing chamber (kWh/hour)
= Length of a pallet (feet)
= = Labor cost to lay the components on the pallet (dollars/component)
= Maximum length of component type (feet)
= = Number of batches or cycles
= = total components
Unused pallet space
L
W
PC products
Li
Wi

## Slide 11
=Loading and unloading time of a component (hours/component)
= Total curing time for a batch of PC components including loading and unloading the kiln (hours/batch)
= Deadline of component (a given point on timeline)
= Maximum width of component type (feet)
= Width of a pallet (feet)
(d) System Variables:
= Number of batches using layout (pallets)
= Number of component type
It may be stated that LW is the area per pallet (i.e., ft2/pallet) and is the area required by component (i.e., ft2/component).
The terms batch or cycle are used interchangeably to mean all components of pallets that are fed into the kiln once for curing.
3. Model Development

## Slide 12
The total energy cost for curing the PC components is
dollars.
Energy cost can be estimated as
= dollars
where is number of batches and
b is the batch size.
Total cost of loading and unloading the components on all pallets is
= dollars
where total number of components).
3. Model Development

## Slide 13
CCM Formulation
The curing cost minimization (CCM) model is composed of energy cost and labor cost and they are obtained here with:
  = The optimal number of pallets,
  = A set of PC components per pallet (layout configuration) to minimize the cost of curing operations.
CCM:
(1)
The objective function (CCM) in equation (1) represents the total associated cost of the curing process of PC components.
3. Model Development

## Slide 14
CCM Formulation
Subject to
(1a)
3. Model Development
*Courtesy: olenbetong.ru
*Courtesy: elematic.com
Total area of PC components will be less than pallet area

## Slide 15
CCM Formulation
(1b)
(1c)
Equation (1c) ensures that production scheduling complies with the delivery deadlines of PC components.
3. Model Development
*Courtesy: olenbetong.ru
Total number of required component type 𝒊 must meet the order agreement.

## Slide 16
CCM Formulation
(1d)
(1e)
Equation (1e) represents the decision variables.
3. Model Development
Li
Wi
Length of PC components having the maximum span are less than the diagonal of the pallet.

## Slide 17
Curing Cost Minimization (CCM) Model
(1)
Subject to
  (1a)
  (1b)
  (1c)
   (1d)
(1e)
3. Model Development

## Slide 18
4. Example: PC Slabs and Beams Manufacturing
Table 1.
Variables | Value | Units
b | 2 | pallets/batch
 | 0.175 | $/kWh
 | T | components
 | 36 | kWh/hour
 | 30 | Feet
 | 40 | $/hours (Labor cost)
 | 0.25 | hours/component (loading/unloading)
 | T | feet
 | = | Number of batches (or cycles)
 |  | Components (total)
 | 10 | hours
 | 8 | hours/batch (power)
 | T | hours
 | T | feet
 | 25 | feet
Variables | Value | Units
b | 2 | pallets/batch
 | 0.175 | $/kWh
 |  | components
 | 36 | kWh/hour
 | 30 | Feet
 | 40 | $/hours (Labor cost)
 | 0.25 | hours/component (loading/unloading)
 |  | feet
 |  | Number of batches (or cycles)
 |  | Components (total)
 | 10 | hours
 | 8 | hours/batch (power)
 |  | hours
 |  | feet
 | 25 | feet

## Slide 19
5. Computational Result
Using the data in Table 1, the CCM problem can be numerically formed as follows
(2)
Subject to
(2a)
(2b)
(2c)
(2d)
and integers (2e)

## Slide 20
The optimal number of pallets obtained for layout 1 and 2 as .
That means, if 2 types of layout configurations (i.e., n = 2) are considered, then
pallets of configuration 1 with components
pallets of configuration 2 with components
So, the pallet’s component-assignment matrix, A= = . This indicates, the number of component type placed in layout according to this optimal solution.
and by following this, the minimum curing cost will be
= $666.00
5. Computational Results

## Slide 21
6. Computational Performance
The computation input data and the output results are provided in Table 2 wherein only the changed values are reported in input data column and the rest of the parametric values are chosen from Table 1.
Table 2 Random Instances
Problem # |  | Variables | Input Data | Optimal Solutions |  |  | 
 |  |  |  |  |  | ($) | CPU†(sec)
1 | (a) |  | T |  | (5,1) | 651.20 | 22.79
 | (b) |  | T |  | (2,4) | 711.20 | 58.43
 | (c) |  | T |  | (1,5) | 731.20 | 45.06
2 | (a) |  | T, T) |  | (3,1) | 640.80 | 20.95
 | (b) |  | (T, T) |  | (1,5) | 691.20 | 29.51
3 | (a) | L, W | (30,25) |  | (1,5) | 691.2 | 4.73
 | (b) | L, W | (35,30) |  | (2,1) | 575.6 | 6.25
 | (c) | L, W | (65,60) |  | (1,1) | 550.4 | 5.99
Problem # |  | Variables | Input Data | Optimal Solutions |  |  | 
 |  |  |  |  |  |  | CPU†(sec)
1 | (a) |  |  |  | (5,1) | 651.20 | 22.79
 | (b) |  |  |  | (2,4) | 711.20 | 58.43
 | (c) |  |  |  | (1,5) | 731.20 | 45.06
2 | (a) |  |  |  | (3,1) | 640.80 | 20.95
 | (b) |  |  |  | (1,5) | 691.20 | 29.51
3 | (a) | L, W | (30,25) |  | (1,5) | 691.2 | 4.73
 | (b) | L, W | (35,30) |  | (2,1) | 575.6 | 6.25
 | (c) | L, W | (65,60) |  | (1,1) | 550.4 | 5.99

## Slide 22
6. Computational Performance
From the research perspective, the computational performance results (Table 2) were analyzed and found out the following points:
When the demand () per PC components increases, the curing cost also increases as well as the computational time.
When the length and width () of PC components increases, the curing cost and CPU time also increase but at comparatively lower rate.
If more components are assigned on the pallet, fewer pallets are needed and so is the batch sizes leading to lesser cost (according to the 3rd row of Table 2).

## Slide 23
7. Future Work
This mathematical model will be used to incorporate industry data in collaboration with LTRC (Louisiana Transportation Research Center).
With increasing demand and dimensions of the PC components, CPU time also get increased. So, a heuristic approach will be followed to get the optimal layout configuration to reduce curing cost.
The model will be revised to focus on the most critical variables that can reduce curing costs.
8. Application and Scope
This optimization ensures that each component is evenly cured, which is vital for achieving consistent material strength and structural integrity.
The economic efficiency achieved through the model not only lowers the initial project costs but also reduces the lifecycle expenses associated with maintenance and repairs, supporting long-term sustainability.

## Slide 24
9. Working Papers
1. Mazumder, A. and Sarker, B. R. (2024a), “Developing an interpretive structural model for factors affecting cost effectiveness, reliability and sustainability of precast concrete,” Working Paper #1 (outcome of QPR-1, January 1 - March 31, 2024).
2. Mazumder, A. and Sarker, B. R. (2024b), “Optimizing Pallet Capacity Utilization to Minimize Curing Cost in Precast Concrete Manufacturing,” Working Paper #2 (Outcome of QPR-2, April 1 - June 30, 2024).

## Slide 25
10. References
Chan, W. T., & Hu, H. (2002). Production scheduling for precast plants using a flow shop sequencing model. Journal of computing in civil engineering, 16(3), 165-174.
Dawood, N. N. (1995). Scheduling in the precast concrete industry using the simulation modelling approach. Building and Environment, 30(2), 197-207.
de Athayde Prata, B., Pitombeira-Neto, A. R., & de Moraes Sales, C. J. (2015). An integer linear programming model for the multiperiod production planning of precast concrete beams. Journal of Construction Engineering and Management, 141(10), 04015029. Mazumder, A. and Sarker, B. R. (2024), “Optimizing Pallet Capacity Utilization to Minimize Curing Cost in Precast Concrete Manufacturing,” Working Paper #2 [Trans-IPIC QPR-2 (LS-23-RP-04), April 1 - June 30, 2024].
Mazumder, A. and Sarker, B. R., “Factors of the Precast Concrete Supply Chain: An Interpretive Structural Modeling Approach,” presented at the Graduate Research Conference (GRC), Students’ Union, Louisiana State University, Baton Rouge, LA on April 30, 2024.
Mazumder, A. and Sarker, B.R., “Exploring Interdependencies of Factors in Precast Concrete Supply System: An Interpretive Structural Modeling Approach,” poster presented at the DOT TRANS-IPIC Workshop (Grant #LS-23-RP-04), Big Ten Conference Center, 5440 Park Place, Rosemont, IL, April 22, 2024.
Sarker, B.R. (2023). Developing A Cost-Effective, Reliable, and Sustainable Precast Supply System under Price Volatility and Uncertainty of Material Supply. A proposal submitted to the DOT/Trans-IPIC, Grant#LS-23-RP-04
Wang, D., Liu, G., Li, K., Wang, T., Shrestha, A., Martek, I., and Tao, X. (2018). Layout optimization model for the production planning of precast concrete building components. Sustainability, 10(6), 1807.

## Slide 26
Thank You!