## Slide 1
TRANS-IPIC August Research Webinar (August 22, 2025)
By
Bhaba R Sarker
and
Anik Mazumder
Louisiana State University
bsarker@lsu.edu & amazum3@lsu.edu
Developing An Integrated Inventory and Delivery Planning System for Precast Concrete to Minimize Total Cost under Probabilistic Demand of Perishable Materials

## Slide 2
Outline
Introduction: Perspectives on PC
Existing Facility
Research Gaps
Precast Raw Materials Handling
Model Development
An Industrial Problem
Computational Performance
Managerial Impact
Future Works
Working Papers
References
TRANS-IPIC August Research Webinar

## Slide 3
1. Introduction
Optimized Precast Concrete (PC) Supply System
Refers to a coordinated, cost-effective, and sustainable framework
Integrates all stages of the supply chain:
(RM procurement production installation construction site)
Considers uncertainty in demand, lead time, and perishability.
Benefits
Technical benefits: High quality & durability, improved structural performance
Process benefits: Accelerated construction, just-in-time delivery
Systematic benefits: Enhanced reliability, improved supply chain coordination
Economic benefits: Cost savings, efficient resource utilization, sustainability.

## Slide 4
Importance of efficient PC supply system in durable Transportation Infrastructures:
1. Introduction
TRANS-IPIC August Research Webinar
To prevent construction delays
For proper structural performance
Improved coordination and workflow
Optimized delivery schedules
Good PC handling practices
Ensures proper installation of PC
Minimized idle time
Timely delivery of RM & PC Components
Improved coordination between production & installation
*Courtesy: Waskey
*Courtesy: GAINEY’S

## Slide 5
Raw Materials Inventory
Production
Internal Molding of PC Products
External Molding of PC Products
Internal Finished PC Inventory
External Finished PC Inventory
Procurement of RM
Manufacturing Facility
Construction Sites
2. Existing Facility
*https://precast.org/blog/the-cost-of-components-test-for-precast-concrete-structures/
Raw materials (RM) typically accounts for approx. 40-60% of total production cost (Ref. NPCA*)
TRANS-IPIC August Research Webinar

## Slide 6
3. Research Gaps
RM procuring for PC production
Improper coordination between vendor & manufacturer
Consideration of demand as constant
Constant lead time consideration between order placement & material receipt
Transportation of PC components
Delay in PC component delivery to construction sites
Uncontrolled expenses in transporting vehicles (e.g., flatbed, trucks) and shared resources (cranes, forklifts)
Improper scheduling reliability
Research Gap 1
Research Gap 2
TRANS-IPIC August Research Webinar

## Slide 7
PC Manufacturing Facility
RM Procurement
TRANS-IPIC August Research Webinar
Order for RM
Order for PC
PC Transportation
Construction Site
PC Material Vendor
4. Raw Materials (RM) Inventory Handling

## Slide 8
4. Raw Materials (RM) Inventory Handling
TRANS-IPIC August Research Webinar
Existing Challenges
If travel/lead time of PC raw material, shelf-life of material,
Intact, angular chunks
Uniformly sized
Proper strength
Loose mix
Moisture ingress
Reduced binding strength
Shortened infrastructure lifespan
USE OF DEGRADED RAW MATERIAL
More frequent maintenance & traffic disruptions

## Slide 9
Research Objectives (RO)
RO1: To minimize the integrated cost of precast material vendor & manufacturer by
Determining optimal order quantities
Developing cooperative inventory policy
Considering uncertain demand and lead times along with perishability of precast materials
TRANS-IPIC August Research Webinar

## Slide 10
TRANS-IPIC August Research Webinar
RO2: To minimize the total cost of precast concrete delivery (PCD) for precast manufacturing facilities by
Determining optimal number of shipments
Determining optimal shipment quantities based on different demand and travel time scenarios
Research Objectives (RO)

## Slide 11
5. Model Development (RO1)
(RO1) The integrated total inventory cost,
Cost for vendor
Cost for manufacturer
Ordering quantity
Reorder point
No of shipments
TRANS-IPIC August Research Webinar
Assumptions:
Probabilistic lead time following distribution within range
Demand is variable following probability distribution between
Nature of precast material is time-sensitive with certain shelf-life
Theorem 1: If the delivery lot arrives beyond the shelf-life , material vendor bears the maximum cost burden, not the manufacturer i.e., .
Theorem 2: If delivery lot arrives within shelf-life , is strictly convex.

## Slide 12
5. Model Development (RO1)
(RO1) The integrated total inventory cost,
Optimal ordering quantity, , is a collection of multiple non-linear terms.
At optimal , optimal number of shipments,
TRANS-IPIC August Research Webinar
Per unit holding cost of vendor
Expected holding cost of manufacturer
Per unit lost sales of manufacturer
Optimal reorder point can be found from following equation:

## Slide 13
6. An Industrial Problem (RO1)
*Original Data is changed a little bit to avoid proprietary conflict of the PC mfg. company
TRANS-IPIC August Research Webinar
Parameter | Description | Value
 | Manufacturer ordering cost per cycle | 1000
 | Vendor ordering cost per cycle | 3400
 | Manufacturer's holding cost per unit per cycle | 80
 | Vendor's holding cost per unit per cycle | 40
 | Perishability cost per unit (shelf-life expiration) | 65
 | Backordering cost per unit short | 70
 | Penalty cost per unit for delayed or perished product | 6190
 | Penalty time-scaling factor | 0.75
 | Additional penalty multiplier beyond shelf-life | 0.80
 | Revenue loss per unit of unmet demand | 500
 | Revenue decay rate due to delay | 0.03
 | Lower bound of demand distribution (units/day) | 2500
 | Upper bound of demand distribution (units/day) | 4400
 | Minimum lead time (days) | 0.02
 | Maximum lead time (days) | 0.08
 | Shelf-life of raw material (in years ≈ 5.5 months) | 0.46
Parameter | Description | Value
 | Manufacturer ordering cost per cycle | 1000
 | Vendor ordering cost per cycle | 3400
 | Manufacturer's holding cost per unit per cycle | 80
 | Vendor's holding cost per unit per cycle | 40
 | Perishability cost per unit (shelf-life expiration) | 65
 | Backordering cost per unit short | 70
 | Penalty cost per unit for delayed or perished product | 6190
 | Penalty time-scaling factor | 0.75
 | Additional penalty multiplier beyond shelf-life | 0.80
 | Revenue loss per unit of unmet demand | 500
 | Revenue decay rate due to delay | 0.03
 | Lower bound of demand distribution (units/day) | 2500
 | Upper bound of demand distribution (units/day) | 4400
 | Minimum lead time (days) | 0.02
 | Maximum lead time (days) | 0.08
 | Shelf-life of raw material (in years ≈ 5.5 months) | 0.46
Variable | Description | Optimal Value
 | Number of Shipments | 2 shipments
 | Order Quantity | 364 units
 | Reorder Point | 284 units
 | Total Cost | $ 60186.94
Variable | Description | Optimal Value
 | Number of Shipments | 2 shipments
 | Order Quantity | 364 units
 | Reorder Point | 284 units
 | Total Cost | $ 60186.94
(Shipments) | (tons of PPC) | (tons of PPC) | ($/year)
1 | 554 | 283 | 60849.74
2 | 364 | 284 | 60186.94
3 | 285 | 284 | 62124.08
1 | 554 | 283 | 60849.74
2 | 364 | 284 | 60186.94
3 | 285 | 284 | 62124.08
, >
The PC mfg. facility faces minimum integrated inventory cost when 2 shipments are sent from the vendor to manufacturer
Optimal values for and

## Slide 14
6. An Industrial Problem (RO1)
TRANS-IPIC August Research Webinar
Parameter | Values | (tons) | ($/year)
 | 500 | 333 | 56,529.04
 | 750 | 349 | 58,397.96
 | 1000† | 364* | 60,186.94*
 | 1250 | 378 | 61,905.44
 | 1500 | 582 | 63,094.39
 | 1700 | 446 | 52,175.87
 | 2550 | 503 | 56,747.34
 | 3400† | 364* | 60,186.94*
 | 4250 | 388 | 63,070.65
 | 5100 | 410 | 65,785.82
 | 250 | 364 | 58,172.79
 | 375 | 364 | 59,179.86
 | 500† | 364* | 60,186.94*
 | 625 | 364 | 61,194.01
 | 750 | 364 | 62,201.09
 | 3095 | 363 | 59,779.45
 | 4642.5 | 363 | 60,017.48
 | 6190† | 364* | 60,186.94*
 | 7737.5 | 364 | 60,318.71
 | 9285 | 364 | 60,426.59
Parameter | Values |  | 
 | 500 | 333 | 56,529.04
 | 750 | 349 | 58,397.96
 | 1000† | 364* | 60,186.94*
 | 1250 | 378 | 61,905.44
 | 1500 | 582 | 63,094.39
 | 1700 | 446 | 52,175.87
 | 2550 | 503 | 56,747.34
 | 3400† | 364* | 60,186.94*
 | 4250 | 388 | 63,070.65
 | 5100 | 410 | 65,785.82
 | 250 | 364 | 58,172.79
 | 375 | 364 | 59,179.86
 | 500† | 364* | 60,186.94*
 | 625 | 364 | 61,194.01
 | 750 | 364 | 62,201.09
 | 3095 | 363 | 59,779.45
 | 4642.5 | 363 | 60,017.48
 | 6190† | 364* | 60,186.94*
 | 7737.5 | 364 | 60,318.71
 | 9285 | 364 | 60,426.59
Sensitivity Analysis of the parameters from industrial data

## Slide 15
6. An Industrial Problem (RO1)
TRANS-IPIC August Research Webinar
SI | (units/year) | (days) | (tons) | (tons) | (shipments) | ($/year) | CPU time (s)
1 | ) |  | 363.80 | 283.78 | 2 | 60,186.90 | 9.26
2 |  |  | 360.47 | 275.45 | 2 | 59,169.10 | 6.62
3 |  |  | 231.12 | 179.62 | 2 | 37,304.60 | 2.77
4 |  |  | 262.13 | 167.35 | 2 | 44,133.70 | 8.25
5 |  |  | 374.88 | 174.29 | 1 | 42,648.60 | 6.64
6 |  |  | 646.00 | 444.05 | 1 | 82,351.90 | 7.02
7 |  |  | 677.41 | 446.90 | 1 | 81,594.90 | 50.71
8 |  |  | 262.92 | 170.91 | 2 | 42,434.90 | 88.57
9 |  |  | 234.98 | 140.54 | 2 | 37,169.40 | 73.60
SI |  |  |  |  |  |  | CPU time (s)
1 |  |  | 363.80 | 283.78 | 2 | 60,186.90 | 9.26
2 |  |  | 360.47 | 275.45 | 2 | 59,169.10 | 6.62
3 |  |  | 231.12 | 179.62 | 2 | 37,304.60 | 2.77
4 |  |  | 262.13 | 167.35 | 2 | 44,133.70 | 8.25
5 |  |  | 374.88 | 174.29 | 1 | 42,648.60 | 6.64
6 |  |  | 646.00 | 444.05 | 1 | 82,351.90 | 7.02
7 |  |  | 677.41 | 446.90 | 1 | 81,594.90 | 50.71
8 |  |  | 262.92 | 170.91 | 2 | 42,434.90 | 88.57
9 |  |  | 234.98 | 140.54 | 2 | 37,169.40 | 73.60
Random examples with different distributions for demand & lead time

## Slide 16
TRANS-IPIC August Research Webinar
5. Model Development (RO2)
Mathematical formulation is required
for precast concrete delivery (PCD) from which:
Optimal number of shipments of contracted vehicles
Optimal shipment quantities
Shipment starting times will be determined
(RO2) Objective function for minimizing total cost of PC delivery (PCD),
Fixed vehicle contracting cost
Fixed resource contracting cost
Scenario based shipping cost
Penalty cost for missing delivery deadline
Penalty cost for unmet demands

## Slide 17
(RO2) Objective function for minimizing total cost of PC delivery (PCD),
TRANS-IPIC August Research Webinar
First Stage Constraints:
and
Second Stage Constraints:
,
5. Model Development (RO2)
Fixed cost of assigning vehicles/vessels
Limited resource allocation
Demand fulfillment for PC components in each project
Limited vehicles/vessels allocation
Limited capacity of vehicles/vessels
Timeline constraints for projects
Non-overlapping shipments for same component in same project
Delivery deadlines constraint

## Slide 18
(RO2) Model PCD,
TRANS-IPIC August Research Webinar
Second Stage Decision Variables
Tons of PC from batch shipped via mode in scenario
Unmet demand for batch in scenario
Start time for shipment of batch shipped via mode in scenario
Completion time for shipment of batch shipped via mode in scenario
First Stage Decision Variables
Number of vehicles (or vessels) contracted for mode .
Number of shared resource units (e.g., cranes, loading equipment) allocated for resource type
5. Model Development (RO2)
Decisions that are made before knowing scenario-specific values like demand or travel times
Decisions that are taken after realization of uncertainty of every scenarios

## Slide 19
6. An Industrial Problem (RO2)
TRANS-IPIC August Research Webinar
Parameter | Description | Value / Range | Unit
 | Number of road projects | 10 | projects
 | Number of precast component types | 5 | types
 | Batches per project | 3 | batches
 | Transportation modes | 3 (flatbed, barge, rail) | modes
 | Demand–travel‑time scenarios | 100 | scenarios
 | Shared resources (cranes/gantries) | 5 | units
 | Demand for project , comp , batch in scenario | Uniform [50, 80] | tons
 | Realized travel time via mode in scenario | Uniform [3, 10] | hours
 | Capacity per vehicle of mode | [20; 25; 30] | tons
 | Unit transport cost per ton by mode | [10; 15; 8] | $/ton
 | Fixed contract cost per vehicle of mode | [1 200; 1 500; 2 000] | USD
 | Fixed‐cost budget for mode | [15 000; 15 000; 15 000] | USD
 | Cost per shared resource | 500 | USD/unit
 | Availability of resource | 5 | units
 | Max trips per vehicle of mode | [2; 3; 2] | trips
Parameter | Description | Value / Range | Unit
 | Number of road projects | 10 | projects
 | Number of precast component types | 5 | types
 | Batches per project | 3 | batches
 | Transportation modes | 3 (flatbed, barge, rail) | modes
 | Demand–travel‑time scenarios | 100 | scenarios
 | Shared resources (cranes/gantries) | 5 | units
 |  | Uniform [50, 80] | tons
 |  | Uniform [3, 10] | hours
 |  | [20; 25; 30] | tons
 |  | [10; 15; 8] | $/ton
 |  | [1 200; 1 500; 2 000] | USD
 |  | [15 000; 15 000; 15 000] | USD
 |  | 500 | USD/unit
 |  | 5 | units
 |  | [2; 3; 2] | trips
Project information
10 road projects, each requiring 3 batches of 5 types of PC
Available mode of transportation: flatbed truck, barge, rail.
Vehicle capacities, per-ton costs, fixed contract budgets, and shared-resource limits set to industry-typical values
Two‐stage PCD model
  Decisions: (vehicles) and (resources)
  Objective: Minimize fixed cost + expected penalties
*Original Data is changed a little bit to avoid proprietary conflict of the PC mfg. company

## Slide 20
6. An Industrial Problem (RO2)
TRANS-IPIC August Research Webinar
1. Scenario Sampling
Approximate expected recourse cost
  Sample S' scenarios (e.g., 20 of 100)
  Compute penalties per scenario:
  • Greedy batch assignment to modes
  • Unmet demand () and delays ()
  Average penalty over samples
2. Generic Algorithm (GA) operators
Initialize 30 random integer vectors within the vehicle/resource bounds.
Selection of parent solutions
Polynomial mutations
Duplicate eliminations
Termination after 50 generation by returning the optimal result

## Slide 21
6. An Industrial Problem (RO2)
TRANS-IPIC August Research Webinar
Mode | Count
Flatbed | 12
Barge | 9
Rail | 6
Resource | Units
Resource 1 | 2
Resource 2 | 4
Resource 3 | 4
Vehicle Contracted
Resource Allocated

## Slide 22
8. Summarized Result
Optimized raw material orders
Avoid overstock and cut storage costs
Reduced project delays
Assess cost impact from demand and lead-time shifts
Improved inventory control with proper consideration of shelf-life
Managerial Impact
Optimal order and reorder quantities to minimize the integrated total cost of precast vendor & manufacturer
Handled generic distributions for material demand and material travel time
Minimized precast concrete delivery cost
Captured shelf-life behavior of PC material in our optimal policy
TRANS-IPIC August Research Webinar

## Slide 23
9. Future Works
Production
Internal Molding of PC Products
External Molding of PC Products
Internal Finished PC Inventory
External Finished PC Inventory
Manufacturing Facility
Construction Sites
?
Batch production system considering raw materials conversion factor
More general scenarios of transporting components
Disruptions in transportation and/or construction and installation process
TRANS-IPIC August Research Webinar

## Slide 24
10. Working Papers
Mazumder, A. and Sarker, B.R. (2025a), “Determining optimal variable order quantities of raw materials for precast concrete production considering demand variability and uncertain material prices," Paper-1 (LS-23-RP-04), Submitted to ASCE: Journal of Construction Engineering & Management. 1st submission: July 16, 2025 (COENG-17929)
Mazumder, A. and Sarker, B. R. (2025c), “Optimal Vendor-Manufacturer Coordination for Perishable Precast Materials Under Stochastic Demand and Lead-Time Uncertainty,” Paper-4 (LS-24-RP-01), QPR Y2-1 (January 1 - March 31, 2025). Submitted to International Journal of Production Economics. 1st submission: August 19, 2025 (PROECO-D-25-02726)
Mazumder, A. and Sarker, B. R. (2025b), “An Optimal Delivery System of Multiple Precast Components for Multiple Construction Sites of Transportation Infrastructure,” Working Paper-3 (LS-24-RP-01), QPR Y2-1 (January 1 - March 31, 2025). Intended for ASCE: Journal of Transportation Engineering.
Quarterly Progress Reports (QPR) Submitted
Sarker, B.R and Mazumder, A., “Optimizing Precast Concrete Supply Logistics Systems under Variable Demand and Probabilistic Delivery Time to Enhance Reliability, Sustainability and Cost-effectiveness: Activity and Network Modeling," QPR-Y2-1, January 1 – March 31, 2025 (LS-23-RP-04 /LS-24-RP-01), Year-2, submitted to TRANS-IPIC/UTC.
Sarker, B.R and Mazumder, A., “Optimizing Precast Concrete Supply Logistics Systems under Variable Demand and Probabilistic Delivery Time to Enhance Reliability, Sustainability and Cost-effectiveness: Precast Concrete Delivery (PCD) Modeling," QPR-Y2-2, April 1 – June 30, 2025 (LS-23-RP-04/LS-24-RP-01), Year-2, submitted to TRANS-IPIC/UTC.
TRANS-IPIC August Research Webinar

## Slide 25
Anvari, B., Angeloudis, P., and Ochieng, W. Y. (2016). A multi-objective GA-based optimisation for holistic manufacturing, transportation, and assembly of precast construction. Automation in Construction, 71, 226-241.
Arashpour, M., Wakefield, R., Lee, E. W. M., Chan, R., and Hosseini, M. R. (2016). Analysis of interacting uncertainties in on-site and off-site activities: Implications for hybrid construction. International Journal of Project Management, 34(7), 1393-1402.
Hidayawanti, R. and Latief, Y. (2023). Raw Material Optimization with Neural Network Method in Concrete Production on Precast Industry. GEOMATE Journal, 24(102): 10-17.
Hossain, M. S. J., Ohaiba, M. M., & Sarker, B. R. (2017). An optimal vendor-buyer cooperative policy under generalized lead-time distribution with penalty cost for delivery lateness. International Journal of Production Economics, 188, 50-62.
Im, K. S., Han, S. H., Koo, B., and Jung, D. Y. (2009). Formulation of a pull production system for optimal inventory control of temporary rebar assembly plants. Canadian Journal of Civil Engineering, 36(9), 1444-1458.
Kong, L., Li, H., Luo, H., Ding, L., Luo, X., and Skitmore, M. (2017). Optimal single-machine batch scheduling for the manufacture, transportation, and JIT assembly of precast construction with changeover costs within due dates. Automation in Construction, 81, 34-43.
11. References
TRANS-IPIC August Research Webinar

## Slide 26
Roy, M. D., & Sarker, B. R. (2021). Optimizing a supply chain problem with nonlinear penalty costs for early and late delivery under generalized lead time distribution. Computers & Industrial Engineering, 160, 107536.
Saptadi, S., Zahra, H. A., Arvianto, A., Wicaksono, P. A. and Budiawan, W. (2023). Inventory Planning and Control Method for Cement Raw Material with Material Requirement Planning (MRP). International Journal of Applied Science and Engineering Review (IJASER), 4(3): 18-31.
Sarker, B. R. and Balan, C. V. (1996). Operations planning for kanbans between two adjacent workstations. Computers and Industrial Engineering, 31(1-2): 221-224.
Sarker, B. R., Baylot, E. A., Green, J. G, and Biswas, P. (2012), “Convoy movement: consideration of turning geometrics for selected vehicle shapes,” ASCE-Journal of Transportation Engineering, 138 (5): pp. 502-511.
Wang, Z., and Hu, H. (2017). Improved precast production–scheduling model considering the whole supply chain. Journal of computing in Civil Engineering, 31(4), 04017013.
Wang, D., Liu, G., Li, K., Wang, T., Shrestha, A., Martek, I., and Tao, X. (2018). Layout optimization model for the production planning of precast concrete building components. Sustainability, 10(6), 1807.
TRANS-IPIC August Research Webinar
11. References

## Slide 27
PC Manufacturer
Construction Site
Flatbed, total 8 trips
88.3% utilization
Truck, total 5 trips
97% utilization

## Slide 28
Thank You!